## Slide 1
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 1 / 24
Experimental and theoretical study of pattern identification
in physical systems with O(2) symmetry
Rory Hartong-Redden
adviser
Professor Rouslan Krechetnikov
Department of Mechanical Engineering

## Slide 2
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 2 / 24
Motivation: the drop splash problem

## Slide 3
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 3 / 24
Motivation: the drop splash problem
1. Physical setup: liquid with known properties
2. Geometry: droplet height, diameter, film thickness
Edgerton’s “milk coronet,” 1936
The three stages of crown formation. Taken from
R. Krechetnikov, G.M. Homsy. “Crown forming instability in the drop splash problem.” J. Colloid Interface Sci 331 (2009) 555-559.

## Slide 4
June 15, 2010 – p. 4 / 24
Experimental objective
Quantitative description of a rim
1. Spikes lie on a circle
2. Each spike described by an angle
Introduction Experiment Theory Conclusion

## Slide 5
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 5 / 24
Experimental Setup
Components
- two high speed cameras
- precision balance
- pump and syringe
- triggering device (function generator)
- high intensity light (LED bulb)
Notes: LEDTRONICS
PAR38-12X2W-XPW-001S

## Slide 6
Introduction Experiment Theory Conclusion
Stereo calibration and triangulation
1. Stereo triangulation – the determination of 3D points from a pair of
coordinates on an image
2. Requires that cameras be calibrated – implemented using the “Camera
Calibration Toolbox for Matlab” by J.Y. Bouguet
Images used to calibrate each camera. Each checkerboard
June 15, 2010 – p. 6 / 24
Stereo triangulation requires knowledge of the rotation R and translation T between the left and right cameras. Taken from J.Y. Bouguet, “Visual methods for three-dimensional modeling.” PhD thesis, Caltech, 1999.

## Slide 7
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 7 / 24
Experimental discussion
Three inter-related experimental challenges
  1. Focus and depth of field
    a. f-number
b. depth of field
  2. Sufficient lighting and contrast
    a. position and quantity of lighting
b. opacity of liquid
3. Controlled environment
a. stable temperature
b. positioning equipment
Diagram illustrating increasing f-numbers, taken from wikipedia

## Slide 8
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 8/ 24
Data analysis procedure
1. Capture images of drop splash
2. Identify corresponding crown peaks by hand
3. Use stereo triangulation to extract 3D points
4. Project onto plane
5. Project onto circle
6. Project onto circle, calculate angles using
atan2(y/x)
Corresponding spikes labeled by number in left and right images

## Slide 9
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 9/ 24
Data analysis procedure
1. Capture images of drop splash
2. Identify corresponding crown peaks by hand
3. Use stereo triangulation to extract 3D points
4. Rotate into best fit plane
5. Project onto x-y plane
6. Project onto circle, calculate angles using
atan2(y/x)
Result of stereo triangulation, in the reference frame of the left camera

## Slide 10
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 10/ 24
Data analysis procedure
1. Capture images of drop splash
2. Identify corresponding crown peaks by hand
3. Use stereo triangulation to extract 3D points
4. Rotate into best fit plane
5. Project onto x-y plane
6. Project onto circle, calculate angles using
atan2(y/x)
Result of stereo triangulation, in the reference frame of the left camera

## Slide 11
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 11/ 24
Data analysis procedure
1. Capture images of drop splash
2. Identify corresponding crown peaks by hand
3. Use stereo triangulation to extract 3D points
4. Rotate into best fit plane
5. Project onto x-y plane
6. Project onto circle, calculate angles using
atan2(y/x)
2D points in x-y plane, origin coincident with center of best fit circle

## Slide 12
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 12/ 24
Data analysis procedure
1. Capture images of drop splash
2. Identify corresponding crown peaks by hand
3. Use stereo triangulation to extract 3D points
4. Project onto plane
5. Project onto circle
6. Project onto circle, calculate angles using
atan2(y/x)
The result of data analysis procedure: angles, displayed here as points on a circle

## Slide 13
Experimentally determined pattern
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 13 / 24
Theory: patterns
Types of patterns
1. Single-wavenumber patterns
2. Regular patterns composed of single-wavenumber patterns (frustration)
3. Irregular patterns
Two key questions
1. Under what conditions is a regular pattern identifiable?
2. What is the “pattern decomposition”?
Ideal pattern

## Slide 14
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 14 / 24
Definition: single-wavenumber pattern
1. Informally: a set of uniformly spaced points
2. Ideal single-wavenumber pattern, formally:
A single-wavenumber pattern with wavenumber and phase shift

## Slide 15
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 15 / 24
Definition: ideal regular pattern
1. Informally: a superposition of multiple single-wavenumber patterns
2. Ideal regular pattern, formally:
An ideal regular pattern consisting of two single-wavenumber patterns: k=3 (red) and k=4 (blue)

## Slide 16
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 16 / 24
Definition: single-wavenumber pattern with scatter
1. Informally: an ideal single-wavenumber pattern plus some scatter – i.e. the
difference between actual and ideal patterns
2. Single-wavenumber patterns with scatter, formally:
3. Plotting single-wavenumber patterns
  a. Plot coordinates
  b. fitting of line is straightforward, standard statistical analysis applies
  A single-wavenumber pattern with scatter plotted on a circle, and its corresponding representation on a graph

## Slide 17
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 17 / 24
Pattern identification
Theoretical stumbling blocks
1. Scatter (due to goodness of fit and experimental uncertainty)
2. Overlapping patterns (due to resolution, and merging of spikes due to surface tension)
3. Incomplete patterns (patterns which are missing one or more points)
Motivates three questions
1. How do we identify a given pattern as regular?
2. Under what conditions can we identify regular patterns?
3. How do we quantify how regular it is?

## Slide 18
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 18 / 24
Pattern identification: other approaches
1. “Ad hoc” methods
a. by inspection
b. look for regular spacing between elements
2. Fourier transform
  a. not appropriate for data type
b. sampling, aliasing and Nyquist Theorem
3. Complex order parameter
4. Computation approaches
An ideal regular pattern consisting of two single-wavenumber patterns: k=8 (red) and k=12 (blue)

## Slide 19
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 19 / 24
Definition: incomplete patterns
1. Informally: patterns which are regular, but missing one or more points
2. Incomplete patterns, formally:
An incomplete pattern consisting of a single-wavenumber pattern with one point missing

## Slide 20
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 20 / 24
Incomplete patterns
1. Want an incomplete pattern definition which retains phase
and wavenumber information
2. Consider as an example a complete pattern with k=4
a. remove a single point
b. remove two points – leads to trouble

## Slide 21
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 21 / 24
Summary of theoretical results
1. A new theoretical framework for patterns
a. Clear definitions of patterns: single-wavenumber,
regular, irregular
b. Classification of theoretical problems: ideal regular
patterns, patterns with overlaps, incomplete patterns
2. Algorithms – implemented in Matlab
  a. can identify non-overlapping ideal regular patterns
  with and without scatter
Edgerton’s “milk coronet,” 1936

## Slide 22
Introduction Experiment Theory Conclusion
June 10, 2010 – p. 22 / 24
Drop splash video
Formation of a regular crown
Film thickness = 0.88mm
Droplet diameter = 4.4mm
Drop height = 28cm

## Slide 23
Introduction Experiment Theory Conclusion
June 10, 2010 – p. 23 / 24
Application to experimental data: regular crown
1. Formation of a milk crown – experimental data
2. Pattern identification: single-wavenumber pattern
3. Tolerance or scatter:
Experimentally determined pattern – frame 9 from previous video
The result of fitting the experimental pattern to the single-wavenumber pattern with scatter model

## Slide 24
Image taken from Parker Hannifin brochure
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 24/ 24
Conclusions and Future Work
Key results
1. New experimental setup with quantitative
data on rim structure
  2. New theoretical framework for pattern identification
Outstanding issues
1. Further exploration of parameter space
  a. single-wavenumber rims with less scatter
  b. identify a case of “frustration”
  2. Theoretical treatment of incomplete patterns with scatter

## Slide 25
Introduction Theory Experiment Conclusion
June 10, 2010 – p. 25 / 24
Appendix: video of an irregular crown
Formation of an
irregular crown
Drop height = 16cm

## Slide 26
Introduction Theory Experiment Conclusion
June 10, 2010 – p. 26 / 24
Appendix: motivation – frustrated rims
Why are there a certain number of spikes?
1. Along the rim instabilities: Richtmyer-Meshkov instability
2. Superposition of regular patterns = “frustration”
Equal growth rates indicates the possible superposition of three wavenumbers
Image taken from G. Homsy, R. Krechetnikov. “Crown-forming instability in the drop splash problem.”
A frustration picture?

## Slide 27
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 27 / 24
Appendix: single-wavenumber pattern factoring
Example:
A single-wavenumber pattern with k=6 is also:
1. two k=3 patterns
2. three k=2 patterns

## Slide 28
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 28 / 24
Appendix: pattern identification algorithm
For ideal regular patterns with possible overlaps
Key idea: identify all patterns (steps 1-6) and then remove subpatterns (step 7)
Finite differences:

## Slide 29
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 29/ 21
Data analysis example

## Slide 30
Introduction Experiment Theory Conclusion
June 15, 2010 – p. 2 / 21
Presentation Outline
1. Introduction
2. Pattern identification theory
3. Experimental study
Image taken from JFM Online
Image taken from efluids, credit: Abhishek Joshi

## Slide 31
Introduction Theory Experiment Conclusion
June 10, 2010 – p. 3 / 21
Introduction
1. Systems with O(2) symmetry
  a. domain of a circle
  b. Time domain
  c. Spatial domain
2. A different type of data
  a. 1-Dimensional
  b. Patterns which deal with
  order of data points
S. P. Betyaev, Physics Uspekhi